## Slide 1
Lab 02
Usama Bin Imran
Computer Organization and Assembly Language
Notes: 1

## Slide 2
What we studied in previous class?
What is Assembly language?
  Close to computer
  Low level language
  Based on Mnemonics/keywords
Why do we study Assembly language?
  Better/deep understanding of software and hardware
  Optimization of processing time

## Slide 3
Continue…..
High level language
Assembly Code
Object file
Machine Code
Hardware
compiler
Assembler
Linker
Filename.c
Filename.asm
Filename.obj
Filename.exe

## Slide 4
Today’s Agenda
In today’s lab we will undergo the following topics:
  Details of registers
  Assembly instructions
  Addressing Mode
  Directives
  Program Structure, syntax
  Tasks

## Slide 5
Registers
What are registers?
  Temporary storage of data
  Fastest storage area
  Quickly accessible by CPU
  Built into CPU
Why do we study Registers?
  Optimization of processing time

## Slide 6
Registers ( Continue……)
Why we use registers?
  Processor operation slowly involve processing data. This can be stored in memory and accessed from there on.
  However, Reading data from and storing data into memory slows down the processor because it involves complicated processes of sending data request across the control bus.
  Thus, registers are used to optimize the processing time as they are already present in CPU and saves a lot of time.

## Slide 7
Types of Registers
There are 14 types of registers, They include:
  Accumulator register
  Base register
  Counter register
  Data register
  Instruction pointer
  Stack pointer
  Base Pointer
  Flag register
  Source Index
  Destination Index
  Code segment
  Data segment
  Stack segment
  Extra segment
General purpose registers
Special purpose registers
Index Registers
Segment Register

## Slide 8
Assembly Instructions
In order to pass any data to registers we use mov instruction
MOV al, 4
MOV ah, 2
To perform addition and subtraction of numbers, keywords, ADD and SUB are used

## Slide 9
Addressing Modes
There include basically three types of addressing modes, They include:
In register addressing, both the operands are registers.
Operand Reg1, Reg2
For-example:
MOV DX, AX
In Immediate addressing, one of the operand is register and the other one is immediate value.
Operand Reg1, Immediate Value
For-example:
MOV DL, 2
In Memory addressing, one of the operand is register and the other access static data directly i.e (Store address of the memory)
Operand Reg1, [Address]
For-example:
MOV DL, [Address]
Register Addressing :
Immediate Addressing:
Memory Addressing:

## Slide 10
Assembler Directives
.MODEL directive
.STACK directive
.DATA directive
.CODE directive

## Slide 11
.MODEL Directive
It specifies the total amount of memory the program would take.
NAME | SIZE
Tiny | Code + data <= 64KB
Small | Code <= 64KB, Data <=64KB
Medium | Code = Any size, Data <=64KB
Compact | Code <=64KB, Data = Any size
Large | Code = Any size, Data = Any size
Huge | Code = Any size, Data = Any size

## Slide 12
Other Directives
Specifies the storage for stack
Usually used 100h
Define variables to be used in our program
It contains the instructions of the program.
. STACK
. DATA
. CODE

## Slide 13
Program Structure
.model small
.stack 100h
.data
.code
mov ah,4ch
int 21h
end