## Slide 1
Lab 01
Introduction
Usama Bin Imran
Computer Organization and Assembly Language
Notes: 1

## Slide 2
About me
Office: A307
Office hours – to be decided
Email: Usama.imran@isb.nu.edu.pk

## Slide 3
Some Rules
  Deadline of anything wouldn’t ever be extended.
  No retake of assignments, quizzes, and lab tasks.
  Can request a re-checking of any of your evaluation as per following rules: Assignment/Quizzes: 2 days after handing over
  Exam: Same day
  Attendance will not be marked if you come inside the lab after 10 minutes
Notes: 3

## Slide 4
Some Rules
  Submit your work on Google Classroom.
  Email submissions won’t be accepted
Notes: 4

## Slide 5
Dishonesty, Plagiarism
All parties involved in any kind of cheating in any exam (Quizzes, Assignments & Projects) will get negative marks.
Notes: 5

## Slide 6
Tentative Evaluation Breakdown
Assignments | 10
Quizzes | 10
Project | 20
Lab tasks | 20
Final Exam | 40
Total | 100
Grading: Absolute
Notes: 6

## Slide 7
Agenda for today
Why Assembly Language?
Assembler
  Registers
  Instructions
DOSBOX Configuration
Notes: https://ebth-14fa.kxcdn.com/media/W1siZiIsIjIwMTQvMTAvMjAvMjEvMzAvMjcvNzQ0L1RUVF82OTg4LkpQRyJdLFsicCIsInRodW1iIiwiNzgxeDg1NVx1MDAzZSJdXQ/TTT_6988.JPG
7

## Slide 8
Program Translation Sequence
Source code transformation into Machine Code.

## Slide 9
Program Translation Sequence
High level language (C, C++)
Assembly Language
Machine Language
Hardware

## Slide 10: Program Translation Sequence

## Slide 11
Program Translation

## Slide 12
Assembler
Brief Introduction to Assembler

## Slide 13
Assembler
Assembler, A program that converts source-code programs from assembly language to machine language. It generates
    Object file: A machine language translation of the program.
    Linker: Copies sub-routines from link library into object file & produces executable program.
    Debugger: Provides a way for programmer to trace execution of a program and examine the contents of memory.

## Slide 14
The Microsoft Macro Assembler (MASM) is an x86 assembler that uses the Intel syntax for Visual Studio and Microsoft Windows.

## Slide 15
Visual Studio 2022

## Slide 16
Installing Visual Studio
Download “Visual Studio Installer” from Google Classroom
Follow the Video guide provided on Google Classroom
https://www.loom.com/share/895449b27f4a4697acebf6e35b55904f?sid=41d8103d-f68b-4805-8c76-82c57475eb41

## Slide 17
Intel 8086 (Registers)
8086 has total of Fourteen Registers accessible to programmer.
Each register is 16 bits long i.e. it can contain 16-bit binary number at max.
General Purpose/Data Registers (AX, BX, CX, DX).
Index/Pointer registers (SP, BP, SI, DI).
Segment Registers (SS, DS, SS, ES).
Control Registers (Flags, Instruction Pointer).
Notes: 17

## Slide 18
Inside 8086 (Data Registers)
8086 CPU has four 16-bit data registers
  AX - the accumulator register (divided into AH / AL).
  BX - the base address register (divided into BH / BL).
  CX - the count register (divided into CH / CL).
  DX - the data register (divided into DH / DL).
These registers can be used in arithmetic or logic operations and as temporary storage.
The main purpose of a register is to keep a number (variable).
Notes: 18

## Slide 19
Inside 8086 (Registers)
The size of the above registers is 16 bit, it's something like: 0011000000111001b (in binary form), or 12345 in decimal (human) form.
4 general purpose registers (AX, BX, CX, DX) are made of two separate 8 bit registers
  For example if AX= 0011000000111001b, then AH=00110000b and AL=00111001b.
Registers are located inside the CPU, they are much faster than memory. accessing a memory location requires the use of a system bus, so it takes much longer.
Accessing data in a register usually takes no time. therefore, you should try to keep variables in the registers for manipulation.
Notes: 19

## Slide 20
Inside 8086 (Data Registers)
Each data register has a special purpose too.
Register | Special Purpose
AX | Multiply/divide
BX | Index Registers for MOVE
CX | Count Register for String Operations
DX | Port address for IN and OUT
Notes: 20

## Slide 21
Instruction
Assembler converts the instruction in to machine code.
  Machine code is a sequence of bits can be read by the processor.
Tells CPU what to do.
Each instruction has
  Mnemonic (Required)
    Symbolic Code for Instructions or Commands to perform a particular function
      mov, inc, add, sub, mul
  Operand (Optional/Depend on Instruction)
    On which operation is to be performed.

## Slide 22
Lab Tasks
Question: Move the following values in the registers, A, B C and D and observe what values are stored in memory:
Value to be moved | Value in memory
AL, 257 | AL? AH? AX?
AX, 567 | AL? AH?
AH, 255 | AL? AX?
AL, 254 | AX?
BX, 0FF4h | BL? BH?
CX, 1237o | CL? CH?
DL, 01001001b | DL? DH?
DH, 0Ah | DL? DX?
Notes: 22

## Slide 23
Lab Tasks
Question: Move the following values in the registers, A, B C and D and observe what values are stored in memory:
Value to be moved | Value in memory
AL, 25h | AL? AH? AX?
AX, 70ABh | AL? AH?
AH, 10011000b | AL? AX?
AL, 20o | AX?
BX, 11111111b | BL? BH?
CX, 1237h | CL? CH?
DL, 0FFh | DL? DH?
DH, 217 | DL? DX?
Notes: 23

## Slide 24
Thank You :)